Todds plans are great for those who actually understand electronics, but for the rest of us, they are near useless.

So, you will all learn from what I have gleaned during the make & take, conversations with Todd, and my good friend Chris who helped me get my model working by smacking me in the back of the head if I did things wrong.

Some parts were not on the list so that will be fixed in this document. Others described are a little sketchy, so some tips on identifying the parts, orienting them, and hooking them together.

| Diagram ID | Description | Mouser Part # |
| --- | --- | --- |
| Input | Power connector | 6-18vdc |
| IC1 | 555 timer | 3V555IN / KA555I |
| IC2 | Fairchild Regulator | LM317T |
| D1 | Schotkey Diode | 1N5817 |
| D2 | Diode | 1N457 |
| Dn | UV LED | LED5-UV-400-30 |
| Rn | 10Ω ¼ watt resistor | CF1/4LT52R100J |
| R10 | 180K ¼ watt resistor | CF1/4L184J |
| R5 | 47Ω ¼ watt resistor | CF1/4L470J |
| R4 | 1M switching potentiometer | RV16A03-10-15R1-B16 |
| R3 | 100K potentiometer | 043P104 |
| R2 | 1KΩ ¼ watt resistor | CF1/4L102J |
| R1 | 330Ω ¼ watt resistor | CF1/4L331J |
| C1 | 0.1µf ceramic disc capacitor 50v | 140-50U5-104M |
| C2 | 1µf electrolytic capacitor 50v | SME50VB1R0M5X11FT |
| C3 | 0.01µf ceramic disc capacitor 50v | 140-50P5-103K |
| C4 | 0.47µf ceramic disc capacitor 50v | UVP2AR47MDA |
| T1 | Epitaxial Transistor | 2N2102 |